FILO Routing of Messages
# Abstract
FILO (First In Layer Off) routing is inspired by the old UUCP style of source routing by supplying a path for the message to follow in it’s “addressing”. FILO messages are files which are delivered via radio paths (HF, VHF, UHF) using various waveforms. FILO addressing is done as the prefix to the filename if a binary file and as a prefix to a date-time stamp if a plain text file. While fundamentally a semi-manual process, some basic automatic functionality does exists and with control over the radio and data modem, full automation should be possible.
Some skill level on the part of the station operators may be necessary, in that knowing which routes “work” makes such a system flow more smoothly. A modicum of human coordination is often required in emergency communications since many stations are ad hoc and may also be portable. Much of this “what works” knowledge is really only necessary at the leaf nodes of such a network, since once an established station is reached, a more stable network has already been derived for the rest of the path. Intervening operators may also re-route messages as required for delivery success.
The creation of “routing tables” has been tested and thus limits the FILO routing to only ONE relay station. Each intervening station supplies the “next hop” toward the destination station. Thus “home mail drops” could be set up on regional network stations. The test implementation of routing tables includes a station route and a “region” route based on the numeral in the destination station call sign.
# Definitions
Message – A message is defined as a file containing some intelligence which must be transferred from one station or person to another. It may be plain text or a binary file of any type.
FILO Formatter – any application which creates messages for use in a FILO routing system. It is capable of fully addressing the message at the user’s will, or by other means by which said addressing may be semi-automated (such as “routing tables” or “address books”).
INBOX – The INBOX is the input queue to any application which is using FILO routing. All incoming messages are placed into the INBOX and are subsequently tested for the FILO routing indicator, “_V_” in the message filename.
OUTBOX – The OUTBOX is the output queue to any application which is using FILO routing. Any message which has yet to be delivered to it’s destination by this station is stored in the OUTBOX. When a remote station connects to this station, it may poll (query) the OUTBOX for any messages that belong to it’s call sign. Both connected stations may perform this operation and it is called a PULL-PULL SYNC.
PULL-PULL SYNC – an action by two connected stations whereby each station asks the other for any messages which are destined for them. Messages are sent one after the other until there is no more work. The sending station archives each message once the receiving station has acknowledged receipt of it.
# FILO Addressing Format
A message file is created by the FILO formatter in one of (at least) two ways.
1. Textual Messages (mail): The user is prompted for a destination address (in radio terms, call sign) followed by a prompt to gather the Relay station in between (this step could be repeated to build a path of multiple relay stations), followed by a prompt to gather the Subject line for the message, followed by a prompt to gather the Body text of the message. This is combined into a simple e-mail style format of:

Message-ID: 20200430172901Z@AC4IY
Date: Thu, 30 Apr 2020 13:29:01 -0400
TO: KA3YAN
FROM: AC4IY
SUBJECT: The Subject
This represents the body text of the message itself.
This text is saved to a file with the format of: RELAY_V_DESTINATION_yyyymmdd_hhmmss.txt
Ex: AB4MW_V_KA3YAN_20200430_123456.txt which means, “Send this message to AB4MW for delivery to KA3YAN.”
2. File Transfers: The user is prompted for the destination address (call sign). This address is pre-pended to the front of the existing filename (even binary) followed by an underscore followed by “FILE:” and the original filename to be sent. For example: the file smiley.jpg is to be sent to address MYHOUSE. The filename of smiley.jpg is changed to MYHOUSE_FILE:smiley.jpg and then moved or copied to the application’s OUTBOX folder.
If FILO routing is used, the relay chain would be pre-pended to the front of this filename as in 1. above.
Ex: AB4MW_V_KA3YAN_FILE:smiley.jpg which means “Send this file to AB4MW for delivery to KA3YAN.”
# The FILO Routing Function
FILO = First In Layer Off, meaning a message is sent to my station with my call sign as the first one on the front of the filename followed by the indicator text “_V_”, such as “AB4MW_V_…..”. This identifies the message as a FILO routed message.
The FILO system which receives the message spots the “_V_” marker and simply strips the “own” call sign from the front of the filename and moves the message file to the OUTBOX.
Ex: Incoming message “AB4MW_V_KA3YAN_FILE:smiley.jpg” is received in the INBOX. It is transformed to “KA3YAN_FILE:smiley.jpg” and placed into the OUTBOX.
In this manner, if the destination station for the message connects to this FILO system, he will find a message waiting for him and automated/semi-automated message SYNC activities can deliver it.
# FILO Routing Clients
## Basic Functionality

FILO routing message/file clients are capable of a set of required functions to support the routing of messages.
- Application level or Operating System integration so far as to allow the end user the ability to display the contents of the received message file
- Originating a new “mail” message which is a basic textual message between two parties and which is in the standard RFC email style with the 5 basic headers. Message-ID, Date, To, From, Subject, then followed by the body text of the message.
- Originating a new “file transfer” message which allows the user to send any file to another user
- The ability of an operator to re-address a message en route in order to affect delivery
## Optional or Extended Functionality
Other functions which may be included in the FILO routing message/file client might include:
- Automated or semi-automated routing of messages based on “routing tables”, “dictionaries”, or “address books”
- Multiple station routing at origination. A known path could be specified of more than one intervening relay stations
- Encryption of transmitted messages between end points of a station to station link
- E-mail gateway functions to transfer the standard “mail” message format to an e-mail Mail Transfer Agent, and all necessary re-addressing if it is intended for carriage over the Internet